Document Title : SOW for Technical services and supply spare part for mechanical hydraulic governor made by WOODWARD Document Number : MT-SOW-ROT- Owner : Reliability Engineering Section Manager Revision Number : 00 Effective Date :

CONFIDENTIALITY The information contained in this document is confidential to Nghi Son Refinery & Petrochemical Limited Liability Company (NSRP). Accordingly, copyright for this document is retained with NSRP and no copying in any format of this document is permitted without the written permission from NSRP Management.

Signatures *

Prepared By:		______________________________
Name: Mohamed Ahmed Bekhiet Hussien

Title:  Rotating Advisor

Reviewed By:	   ______________________________
Name: Doan Nhat Bang
Title:  Rotating Leader

Reviewed By:	   ______________________________
Name: Nguyen Song Binh
Title:  Deputy Section Manager Reliability Engineering

Approved By:		______________________________
Name: Ben Alfrink
Title:  Division Manager Maintenance

* These signatures apply to entire document

Amendment Table

| Rev. No. | Date | Description | Prepared by | Reviewed by | Approved by |
| --- | --- | --- | --- | --- | --- |
| 00 |  | Initial release | DN Bang | NS Binh | B. Alfrink |

AMENDMENT REPORT FORM

| No. | Item | Original | Revised | Reason |
| --- | --- | --- | --- | --- |

Contents

1.	SUMMARY	5

2.	PURPOSE OF BIDDING	5

3.	SCOPE OF WORK	5

4.	ATTACHMENT	7

# SUMMARY

A mechanical governor is used to sense and control speed of a turbine or engine and is a critical component for the safe and reliable performance of the rotating equipment. The governor should be overhaul and calibration after 20,000 running hours

Malfunction of mechanical governor will affect main driven equipment performance and accordingly process condition

Availability of complete governor set in warehouse for direct replacement purpose will minimize the equipment break down time and improve equipment availability and process productivity

Calibration and function test for refurbished governor need special bench test which affect the repairing duration

09 models of hydraulic governors control 27 steam turbines in NSRP

      - Type: Mechanical Hydraulic Governor

      - Manufacture: WoodWard

      - No of Model: 09

      - No of Equipment: 27

# PURPOSE OF BIDDING

NSRP needs to contract with the Vendor who can provide repairing, calibration, function test for WoodWard hydraulic governors. NSRP wants to contract with them who have a capability for above requirements. NSRP should consider the countermeasure to be “MINIMUM COST “, and “MIMIMUM DOWNTIME” for NSRP plant.

# SCOPE OF WORK

The contractor shall provide full range of mechanical-hydraulic governor services such as repairing, calibration, function test and overhaul with the necessary specialised tools and test equipment to handle a comprehensive range of governors.

Supply spare parts (genuine spare parts) for repair, refurbish and overhaul

Supply full set of WoodWard mechanical hydraulic governors (if NSRP request)

Provide 24/7 phone call service and field service.

  - Requirement of Refurbishing, repair and overhaul services

- The service are include but are not limited to Contractor’s incidental services, tools equipment, handling, transportation including transportation of personnel and materials to and from the Work Site

- Contractor shall prepare and provide all applicable spare parts required (Genuine spare parts), consumable (if needed) for service.

- After inspection, Contractor shall submit the list of spare parts that are required for overhaul or repair to NSRP for review and approval.

- Contractor workshop shall have fully equipped with the highly trained and experienced personnel and specialized tools required to complete repairs and overhauls and comprehensive testing on the full range of Woodward governors type TG and PGD. The contractor is responsible for testing and calibration all tools and equipment if require. The certificates shall be presented to NSRP, when requested

- Arrange transportation 2 ways for equipment from NSRP to contractor WS and return

- The average service turn-around is less than 10 working days (for overhaul and refurbish at Contractor service shop)

- As and when instructed by NSRP, in accordance with NSRP requirements, Contractor will dispatch a field service engineer to perform quick and dependable service in NSRP (between 24 hours if deployment service engineer from domestic or in South East Asian, and within 3-4 days for deployment service engineer from others places). The service engineer will arrive on site prepared with the necessary background information and skills to troubleshoot and efficiently solve problem and make recommendations to maximize control system efficiency and avoid downtime.

- The Contractor shall be available 24/7 (24/7 Phone Call Support Services- 24/7 PCSS) to support trouble shooting of the Equipment malfunctions upon request from NSRP engineers via telephone or email, and the response time must be within 4hrs.

  - Contractor shall submit the final report for this service. The final report shall be mentioned the following but not limited to.

- Work description and maintenance report including inspection record during open equipment

- Criteria for replacement and re-use of all parts

- Measurement Record for all parts based on vendor criteria.

- Calibration and function test certificate record for repaired governor set

- Picture record for the damaged parts.

- Support for Root Cause Analysis if require

- The warranty period shall be 12 months from the date of completion of works are put in regular use.

  - Requirement of spare parts

- All Spare Parts (Genuine spare parts) shall be in new condition and shall have warranty of twelve (12) months from installation or delivery and handover to NSRP staff through duly signed loading/delivery note.

- If required material is obsoleted and confirmed officially by manufacturer, Supplier shall provide recommendation with equivalent material. Any technical deviation between required material and proposed material shall be clearly specified.

- Supplier shall provide technical document for NSRP’s review e.g. material manual, specification, datasheet, ordering information.

- All materials to be supplied shall be 100% new and in the best condition.

- All materials shall be delivered to NSRP’s warehouse at Supplier’s cost. All expenses including custom duties, transportation, and insurance shall be borne by Supplier.

- Certificate of Origin (CO), Certificate of Quality (CQ) and other supporting documents shall be provided by Supplier when material is handed over to NSRP

  - Requirement for Personal

- Submit Curriculum Vitae (CV) for workshop service engineers for this repair. With minimum 05 years practical experience of Wood Ward mechanical hydraulic governor models

- Submit Curriculum Vitae (CV) for site engineer for installation/MRT. With minimum 05 years practical experience of Wood Ward mechanical hydraulic governor models

- Other key person must also have the professional certificate(s) for in accordance with regulations (if any) and have at least 5 years of experience of related work

# Attachment

Attachment-1: WOODWARD’s Governor List in NSRP

| No | Model | Serial No | Rotation Facing Governor End | Rate Speed | Part Number | Remark |
| --- | --- | --- | --- | --- | --- | --- |
|  | TG 611-17 | 19830616 | CW | 2900 | 8516-188 |  |
|  | TG 611-17 | 19830615 | CW | 2900 | 8516-188 |  |
|  | TG 611-17 | 19848497 | CW | 1500 | 8516-186 |  |
|  | TG 611-17 | 19848489 | CW | 1500 | 8516-186 |  |
|  | TG 611-17 | 19848498 | CW | 1500 | 8516-186 |  |
|  | TG 611-17 | 19819977 | CW | 2960 | 8516-188 |  |
|  | TG 611-17 | 20542571 | CW | 1500 | 8516-186 |  |
|  | TG 611-17 | 19712331 | CCW | 1480 | 8516-186 AM |  |
|  | TG 611-13 | 19712180 | CCW | 1484 | 8516-175 |  |
|  | TG 611-13 | 19675597 | CCW | 1479 | 8516-175 |  |
|  | TG 611-13 | 19855233 | CW | 1450 | 8516-176 |  |
|  | TG 611-13 | 19754335 | CW | 1450 | 8516-202 |  |
|  | TG 611-13 | 19225769 | CW | 2970 | 8516-180 |  |
|  | TG 611-13 | 19522535 | CW | 2965 | 8516-180 |  |
|  | TG 611-13 | 19606042 | CCW | 2980 | 8516-179 |  |
|  | PGD | 19624892 | CCW | 1460 | 8577-1490 |  |
|  | PGD | 19626338 | CCW | 1460 | 8577-1490 |  |
|  | PGD | 19622676 | CCW | 1460 | 8577-1490 |  |
|  | TG 611-13 | 19658041 | CCW | 2910 | 8516-179 |  |
|  | TG 611-17 | 19788626 | CW | 1450 | 8516-186 |  |
|  | TG 611-17 | 19509466 | CCW | 1487 | 8516-233 |  |
|  | PGD | 19827069 | CCW | 2980 | 8577-1505 |  |
|  | TG611-13- NEMA A | 19644276 |  |  | 8516-179 |  |
|  |  | 19369673 |  |  | 8516-202 |  |
|  |  | 19369672 |  |  | 8516-202 |  |
|  |  | 20025677 |  |  | 85-16-180 |  |
|  |  | 20102097 |  |  | 8516-180 |  |